## Slide 1: U.S. Antarctic Program Resupply Perspectives
Brian Stone
Antarctic Infrastructure & Logistics

## Slide 2: Why McMurdo Station?
Deep water access for ships
Relatively stable ice edge
Annual sea ice breakout
Access to Ross Ice Shelf and the continent
Critical for access to South Pole & deep field.

## Slide 3: Vessel Operations Early Operation Deep Freeze
Ice edge cargo transfers
McMurdo break-in for fuel resupply
Unpredictable ice conditions increase risk.
Personnel losses
Cargo offload at McMurdo started mid-1960’s.

## Slide 4: Vessel Support Over the Years
1950’s
  US Navy ships
  Navy & USCG operated icebreakers (smaller)
1960’s
  US Navy transfers all icebreakers to USCG
1970s
  NSF assumes full responsibility for USAP.
  USCG commissions Polar-class breakers
1980’s
  Introduction of civilian ships
2000’s
  B-15 iceberg creates need for 2-ship ops
  NSF contracts with FESCO for icebreaker support
  NSF contracts with Sweden for ODEN
Present
  MAERSK PEARY (tanker)
  GREEN WAVE (dry cargo)
  VLADIMIR IGNATYUK (icebreaker)

## Slide 5: Key Considerations for Ships
Icebreaking or ice-strengthened
Must burn light fuels (MGO)
  2011 IMO rule
  Increases cost – limits availability of backups
Self-supporting for offload/onload (limited port facilities)

## Slide 6: Icebreaker Support

## Slide 7: Vessel Support over the years

## Slide 8: Ice Wharves and Piers
Mid-1960’s abandoned ice edge as routine site for cargo offload.
Introduction of containerized cargo meant higher weights and increased risk of ice edge transfers.
Improvements to “Edisto Quay” from 1969-1973.
Ice wharf destroyed in winter storm in 1973.
USAP switched to ice pier. (1973-present)

## Slide 9: Modular Causeway System
Ice pier not suitable for cargo offload
US Army providing MCS and 40-person team to assemble.
Down and back on cargo vessel
3 days setup / 3 days teardown

## Slide 10: USAP Cargo Vessel Movements
Southbound cargo volumes vary greatly with on-ice activities. Construction activity = more weight
Some cargo cannot be easily flown
  Hazardous cargo
  Frozen foods
Rolling stock & breakbulk
Northbound cargo drivers
  Solid & Hazardous waste
  Science cargo
  Outsized items
Backlog of non-hazardous retrograde

## Slide 11: USAP Airlift 1990-2010
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
1990 | 125 | 0 | 0 | 0 | 0 | 0 | 600 | 150 | 150 | 150 | 150 | 150 | 75 | 75 | 75 | 75 | 75 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 90 | 90
2000 | 200 | 0 | 0 | 0 | 0 | 0 | 600 | 150 | 150 | 150 | 150 | 150 | 75 | 75 | 75 | 75 | 75 | 40 | 40 | 40 | 40 | 40 | 40 | 150 | 150 | 150 | 200 | 200
2010 | 500 | 0 | 0 | 0 | 0 | 0 | 400 | 400 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300 | 300
Week of the Season
Available Airlift (1k lbs)

## Slide 12: Transformative Capabilities
Pegasus Runway
  First WINFLY/Late-Season use
  White-ice development 2002 led to year-round wheeled ops by 2004
  Greater flexibility in aircraft types
C-17 Globemaster 3
South Pole resupply capability – traverse and air support